## Slide 1
GC0091
Demand Connection Code
Demand Side Response requirements

## Slide 2: Overview
Summary of DSR under DCC
Draft legal text prepared for DSR (DCC Article 27 – Article 30)
Issues table prepared
Aim to discuss:-
High level drafting
Issues
Concerns
Correct interpretation
Discussion
Next Steps

## Slide 3: Summary of DSR Services under DCC
Not Mandatory but applicable if a party wishes to provide DSR
Remotely Controlled (Instructed)
Demand response Active Power Control
Demand response Reactive Power Control
Demand response Transmission Constraint Management
Autonomously Controlled (Automatic)
Demand Response System Frequency Control
Demand Response Very Fast Active Power Control

## Slide 4: General Issues (1)
Not all DSR providers will be CUSC signatories hence the term User may need changing
How would non CUSC parties be treated or would the Commercial Agreement simply refer to Grid Code and Distribution Code clauses
  ie The Commercial Agreement simply states the Provider must comply with the appropriate clauses of the G Code and D Code
Do we need to define a new term of Commercial Agreement – Would this be equally applicable between Grid Code and D Code
Do we need to define a new term – Aggregator
Art 28(2)(c), (e), (f) (k) and (l) – Demand Units connected below 110kV – it is assumed these issues are caught by National Governance (Ref Art 6 and Art (9)(1)) and do not require explicit reference in the Codes
Standards for Operational Metering and Data Exchange – For Grid Code this would probably be via the RES. For DNO’s this requires further clarification

## Slide 5: General Issues (2)
Art 28(2)(g) Protection limits - Requires workgroup discussion – this clause is unclear
Art 28(2)(j) This is not clear – Requires workgroup discussion
Art 28(2)(k) Rate of change of Frequency – This has been set at 1Hz/s second over 500ms timeframe to ensure consistency with RfG. Consideration needs to be given to performance under times of System stress including fault ride through and consistency with other codes
Art 28(2)(I) Voltage / Frequency signals – Are these issues not already covered by Art 28(2)(d) and Art 28(2)(e).
Art 29(2)(b) As per previous slide Art 28(2)(c) – (k). The same comments also apply to Art 29(2)(b) – (d)
Art 29(2)(g) Not well worded - requires further workgroup discussion
General Glossary and Definitions requires further discussion

## Slide 6: Questions
Do the requirements in Articles 27 – 30 provide sufficient flexibility for all types of providers to offer the services they wish to provide without resulting in undue restrictions
Are any parts of the DCC Demand Side Response provisions unclear.
Is it appropriate to specify minimum requirements in the Grid Code and link any contract to those provisions.
Are any of the requirements unachievable
Do these provisions provide adequate flexibility for Aggregators. Does any work need to be addressed at a GB level to promote the role of Aggregators for DSR provision

## Slide 7: Next Steps
Consider provisional Legal Drafting and seek work group comments
Consider issues and update legal text as necessary
Consider Glossary and Definitions
Repeat process as applied to Articles 27 - 30 for DCC - Articles 12 – 21 in respect of Transmission Connected Demand Facilities, Transmission Connected Distribution Facilities and Distribution Systems
Discussion